## Slide 1: THE CASE STUDY OF CAMPI FLEGREI Managing Volcanic Risk and Unrest Phases
Moderator/ SPEAKER: Giulio ZUCCARO (UNINA-PLINIVS)
SPEAKERS: GIOVANNI MACEDONIO (INGV-OV) - Annamaria Criscuolo (POZZUOLI)
GOBEYOND 2nd WORKSHOP
21-22 April, 2026 – Napoli (Italy)
Aula Magna, Conference Hall, Università degli Studi di Napoli Federico II

## Slide 2: Introduction Campi Flegrei: a complex and evolving multi-risk system
Ongoing volcanic unrest
Seismic swarms
Ground deformation (bradyseism)
Intense degassing
Multi-hazard interactions
Volcanic + seismic processes
High uncertainty and evolving conditions
High exposure
Dense urban environment
Vulnerable building stock
Critical infrastructures
Observed impacts (non-eruptive phase)
Structural damage
Social and economic effects
Living risk system
Understanding the system is essential,
but not sufficient to manage risk

## Slide 3: INTRODUCTION: From hazard understanding to risk management
HAZARD & PROCESSEES
Giovanni Macedonio
VULNERABILITY & IMPACT
Giulio Zuccaro
Emergency Management
Annamaria Criscuolo
(INGV)
(UNINA-PLINIVS)
(POZZUOLI)
Effective risk management requires integration across these domains

## Slide 4: Hazard and Volcanic Processes
Understanding the dynamics of the system
Giovanni Macedonio INGV
National Institute of Geophysics and Volcanology
Italy

## Slide 5: CAMPI FLEGREI CALDERA

## Slide 6: Explosive eruptions (convective or collapsing column)

## Slide 7: Hazard from pyroclastic flows and ash fallout (red and yellow zones)
Ash loading greater that 300 kg/m2, probability 5%
Approved by Regione Campania on 3 April 2015

## Slide 8: HAZARD FROM BRADYSEISM
DL 12 October 2023 n.140

## Slide 9: Seismicity associated with bradyseism

## Slide 10: Deformation from sar interferometry

## Slide 13: The monitoring network of campi flegrei

## Slide 14: Monitoring room of the osservatorio vesuviano (ingv, napoli)
THANK YOU FOR THE ATTENTION

## Slide 15: Vulnerability and Impact Assessment
From hazard to expected impacts and mitigation strategies
Giulio Zuccaro PLINIVS Study Centre
University of Naples Federico II
ITALY

## Slide 16: From Hazard to Ongoing Impact in Campi Flegrei
Campi Flegrei is a multi-hazard system
Ongoing unrest produces relevant non-eruptive impacts (event without eruption)
Risk emerges from hazard, vulnerability and exposure interaction
Need to translate knowledge into decision-support tools
We are not dealing with a potential risk, but with impacts already affecting the system
~ 150 cm uplift since 2005
~85,000 residents exposed
Residents temporarily displaced

## Slide 17: Operational Challenges in a Complex Risk Environment
Coupled processes: seismicity + bradyseism + volcanic dynamics
High urban density and structural vulnerability
Evacuation planning constraints (red and yellow zones)
Uncertainty in evolution and timing of unrest phases
Decision-making is challenged by complexity, uncertainty and scale

## Slide 18: DL 140/2023: A Strategic Response to Volcanic Unrest
Intervention Area
Defined under DL 140/2023
Includes Pozzuoli, Bacoli and western Naples
Characterized by:
  long-term seismicity
  bradyseismic uplift (~20 cm since 2006)
Plan Objectives
National plan for seismic risk prevention in Campi Flegrei
Focus on areas affected by bradyseism and seismicity
Aims to:
  assess vulnerability of the built environment
  define mitigation priorities
From emergency awareness to structured mitigation planning
~85,000 residents
~15,000 buildings
3 municipalities involved

## Slide 19: DL 140/2023: Structure of the Plan
The Plan includes four main components and is coordinated by the Civil Protection Department, with the involvement of institutions, scientific centres and technical professionals:
A comprehensive framework integrating knowledge, assessment and mitigation
Microzonation
Seismic microzonation studies
Private vulnerability
Vulnerability assessment of private buildings (aimed at defining mitigation measures and related costs)
Public vulnerability
Vulnerability assessment of public buildings
Monitoring
Enhancement of seismic and structural monitoring systems
€1.5 million
€3.5 million
€37 million
€0.2 million
Initial mitigation planning

## Slide 20: Vulnerability Assessment of Private Buildings
Large-scale survey of private residential buildings
Based on simplified and progressive assessment procedures
Integration of:
  - PLINIVS rapid survey (areal scale)
  - CARTIS typological classification
  - CARTIS BUILDING: Detailed building inspections
From large-scale screening to building-level understanding

## Slide 21: Spatial Distribution of Seismic Vulnerability
Supporting prioritization of intervention areas
where:
Ek,i​: number of buildings in class (A–D) within cell ;
weight assigned to class , based on a vulnerability scale (D=0.125, C=0.375, B=0.625, A=0.875)
LEGEND:
High Medium
Low Very Low
For the classification of cells based on building vulnerability, a combined approach (Criterion 3) was adopted, integrating:
the absolute index (VA,i), influenced by building density of the area)
and the relative index (VR,i), representing average vulnerability in each cell),
in order to maximize the presence of highly vulnerable buildings (Class A) within high- and medium-priority cells.
Vulnerability Index (i-cell)

## Slide 22: CARTIS Approach for Typological Vulnerability Assessment
From typological survey to vulnerability and risk assessment
Area-based survey of building typologies and structural characteristics
Two complementary levels:
- CARTIS–Compartment → urban scale classification
- CARTIS–Building → detailed building information
Supports:
- typological classification of the building stock
- identification of representative structural models
Provides input for:
- mechanical modelling
- vulnerability classification (A-F)
- cost estimation and mitigation planning

## Slide 23: Risk Mitigation as an Economic Investment
Scenario IMCS VIII |  |  |  |  | 
 | Mitigation Costs [€] | Direct Costs[€] | Indirect Costs [€] | Total Costs[€] | ∆ [%]
No mitigation | – | 663,976,034 | 543,253,119 | 1,207,229,152 | –
Strategy 1 (A→B) | 394,517,606 | 426,205,254 | 348,713,390 | 1,169,436,250 | 3%
Strategy 2 (A→C) | 558,833,792 | 258,594,926 | 211,577,667 | 1,029,006,385 | 15%
Scenario IMCS IX |  |  |  |  | 
 | Mitigation Costs [€] | Direct Costs[€] | Indirect Costs [€] | Total Costs[€] | ∆ [%]
No mitigation | – | 863,337,245 | 706,366,837 | 1,569,704,082 | –
Strategy 1 (A→B) | 394,517,606 | 580,783,375 | 475,186,398 | 1,450,487,380 | 8%
Strategy 2 (A→C) | 558,833,792 | 343,344,025 | 280,917,839 | 1,183,095,655 | 25%
Direct costs: reconstruction of buildings
Indirect costs: service disruption, productivity loss (~45%)
Intangible costs: human losses and social impacts (not monetizable)
Δ factor: measures economic benefit of mitigation (does not include intangible costs → conservative estimate
These results support mitigation investments and enable access to financial support (BEI):
€1.4 billion
(€850M for public infrastructure and €550M for private housing).

## Slide 24: DL 140/2023: From Vulnerability Assessment to Mitigation Actions
Intervention Areas
DL 140/2023 defines the target areas (Pozzuoli, Napoli, Bacoli) and launches the extraordinary seismic vulnerability assessment plan
Support for Private Buildings
€50M allocated (2024–2026) for the repair of unusable residential buildings
Access to Funding
Decree (Nov 2025) defines procedures for accessing incentives for seismic upgrading in vulnerable areas (20 M/yr for 5 years)
Funded Interventions
Seismic improvement, local strengthening, and safety measures for structural and non-structural elements, based on CARTIS priorities
Linking vulnerability assessment to concrete mitigation actions

## Slide 25: MULTI-HAZARD IMPACT-BASED APPROACH
Hazards considered:
🌍 Earthquakes (INGV data)
🌋 Volcanic unrest (bradyseism)
🌫 Ash fall (FALL3D simulations)
Integration:
Hazard-specific data (real-time & scenarios)
Vulnerability
Exposure (building inventory)
Outputs:
Impact maps per hazard
Multi-risk impact scenarios
Prioritization of emergency actions
From “multi-hazard assessment” to “impact-based decision support”

## Slide 26: EASE TOOL: NEAR REAL TIME ASSESSMENT TOOLSǀ EQ

## Slide 27: EASE TOOL: NEAR REAL TIME ASSESSMENT TOOLSǀ AF

## Slide 28: From models to decision support (GOBEYOND)
Integration of models into operational platforms (ARGOS / EASE)
Near real-time impact-based products
Damage scenarios and prioritization of response actions

## Slide 29: FROM KNOWLEDGE TO ACTION
Planning for mitigation. Acting in real time
PLANNING & MITIGATION (DL 140)
Large-scale vulnerability assessment Prioritization of interventions Optimization of resources
RAPID RESPONSE (GOBEYOND)
Near real-time impact scenarios Support to emergency operations Identification of priority areas for response
THANK YOU FOR THE ATTENTION

## Slide 30: Emergency Management and Response
From knowledge to operational action
Annamaria Criscuolo POZZUOLI Municipality
Civil Protection Office
ITALY

## Slide 31: Civil protection activities in emergency management. the bradyseismic crisis in Pozzuoli -
Emergency preparedness
Planning activities and communication to the population
Response Actions
Assistance and reception to the population in emergency areas;
Damage assessment;
Continuity of essential municipal services;
Communications activities
Manages communication with citizens and authorities and data sharing with scientific institutions

## Slide 32: SEISMIC AND BRADYSEISMIC CRISES
The caldera of the Campi Flegrei is characterized by the phenomenon of bradyseism (phases of slow lowering of the ground, alternating with phases of faster uplift), which can be accompanied by seismic activity.
The major recent bradyseismic crises occurred in the periods 1970-1972 and 1982-1984.
In 2005, a new phase of lifting began. Since 2018, the uplift has been accompanied by a gradual increase in seismic activity, both in the number of earthquakes and in their magnitude .
In 2024-2025 due to a new phase of acceleration of the uplift in POZZUOLI many seismic events occurred causing building damaging and fear among the population . The most significant seismic events are :
Time series of weekly elevation changes recorded at the RITE station (Pozzuoli – Rione Terra) from 2000 to June 2025 (Source: Monthly Surveillance Bulletin, June 2025.)
Md=4.0
Md=4.4
Md=4.6
Seismic swarm of May 20th -21th 2024 (168 earthquakes , Mdmax = 4.4)
Seismic swarm of February 15th – 20th 2025 (672 earthquakes , Mdmax = 3.9)
Seismic swarm of March 13th 2025 (44 earthquakes , Mdmax = 4.6)
Seismic swarm of May 13th 2025 (49 earthquakes , Mdmax = 4.4)

## Slide 33: PREPARATION ACITVITIES Emergency Response Plan for the Bradyseism Area
A. Criscuolo (POZZUOLI)
Definition of emergency scenarios and operational response model in the area of intervention for bradyseism (Legislative Decree 140/23);
Implementation of a Communication plan aimed at disseminating knowledge of risks and good civil protection practices;
Identification of safety waiting areas for assistance to population and shelter areas ;
Definition of protocols for building damage assessment (AeDES forms)
Definition of support measures for population in case evacuation is needed.

## Slide 34: WAITING AND SHELTER AREAS
A. Criscuolo (POZZUOLI)

## Slide 35: RESPONSE ACTIVITIES - THE FIRST PHASES' EMERGENCY ACTIVITIES
EVENT
OCCURING
  THE MAYOR CONVENES THE CRISIS UNIT
ACCORDING TO THE SEVERITY OF IMPACTS MAYORS ASSESSES THE ACTIVATION OF COC ( EMERGENCY OPERATIONAL CENTRE)
COMMUNICATIONS ACTIVITIES FOR EMERGENCY MANANGEMENT
  DAMAGE REPORT RECORDING AND TERRITORIAL MONITORING BY THE MUNICIPAL POLICE ANDTHE CIVIL PROTECTION VOLUNTEERS

## Slide 36: COC ACTIVATED

## Slide 37: SETTING UP EMERGENCY WATING AND SHELTER AREAS
Emergency waiting areas set up during the 20th of May 2024 emergency

## Slide 38: DAMAGE REPORTING
Request for post-earthquake usability/structural safety inspection using the appropriate forms (IPP Form)
Planning and scheduling building inspections by the Aedes engineers
Completion of Aedes assessment forms with a habitability outcome
Issuance of an evacuation order in case of uninhabitable conditions

## Slide 39: COMMUNICATION during the emergency phase
Timely communications to the population, with organic and clear content;
Use of diversified communication forms (institutional website, social media, local broadcasters);
Continuous flow of information with all subjects involved in emergency management and with coordination centers

## Slide 40: Lesson Learned

## Slide 41: Civil Protection of Pozzuoli
Municipal volunteer group
A. Criscuolo (POZZUOLI)
THANK YOU FOR THE ATTENTION

## Slide 42: KEY MESSAGEs
Multi-hazard context requires integrated approaches
Impact-based tools can support decision-making in real time
Bridging science and operations remains the main challenge

## Slide 43: Let’s start with a few questions to trigger the discussion…
Considering the high uncertainty of volcanic unrest and eruptive scenarios, what do you see today as the main limitation in translating hazard models (e.g. seismicity, ash fall) into operational tools that can effectively support real-time decision-making?
What are the main challenges in translating impact assessment results (based on vulnerability and exposure) into clear operational priorities for mitigation and emergency response?
From the point of view of local civil protection, what are the main difficulties in transforming scientific and technical information into concrete actions, especially under time pressure and limited resources?
…

## Slide 44: Thank you for your attention.