## Slide 1
GOBEYOND 2nd WORKSHOP
21-22 April, 2026 – Napoli (Italy)
Venue: Aula Magna, Conference Hall, Università di Napoli Federico II
ROUND TABLE 1
Early Warning for Volcanic Eruptions and Tsunamis: From Simulation to Operational Response
Moderator: Anne Lemoine (BRGM)
Speakers: Alessandro Amato (INGV), Ólafur Loftsson (Icelandic Civil Protection), Alberto Armigliato (Università di Bologna)

## Slide 2: Euro-Mediterranean Tsunami Catalogue v2.0
294 entries
6150 BC – 2018
Recent, not included events:
2 May 2020 south of Crete
30 October 2020 Samos
6 February 2023 Turkey –
eastern Mediterranean
Meteo-tsunamis not included!
Maramai et al. (2019)

## Slide 3: Euro-Mediterranean Tsunami Catalogue v2.0
Maramai et al. (2019)
Non-seismic causes:
landslide
volcanic activity

## Slide 4: Euro-Mediterranean Submarine landSlide database (EMSS21)
Urgeles et al. (2021)
https://ls3gp.icm.csic.es/?page_id=553
Deposits
Scars

## Slide 5: Meteotsunamis in the Mediterranean
No structured catalogue exists yet.
From Vilibić et al. (2025)

## Slide 6: Non-seismic tsunami sources in a warning perspective
Warning chain steps | Seismic sources | Non-seismic sources
Source characterisation (in near-real time) | Seismic inversion (typically, 2-5 minutes) | No equivalent standard approach (Volume and rheology are unknown)
Warning time (for the near field) | Minutes (seismic signals travel faster and hence arrive first) | Seconds to minutes (in general, no seismic precursor, with exceptions)
Model uncertainty | Quantifiable (calibrated distributions) | Large epistemic (can lead to a factor 3-5 in amplitude)
Observational (benchmarks) | Large, diverse | Not as many, and often debated

## Slide 7
First Tsunami buoys in NEAMTWS – September 2025

## Slide 8
Stromboli volcano | Pyroclastic flow on the Sciara del Fuoco
Stromboli (Tyrrhenian Sea): tsunami generated by subaerial/submarine gravitational collapses or pyroclastic flows at the Sciara del Fuoco

## Slide 9: Turkey earthquake Feb. 6, 2023 Mag 7.8
Alert levels (maximum) with the current Decision Matrix (approved by UNESCO NEAMTWS in 2016)
Alert levels with the Probabilistic Tsunami Forecast (NOT YET approved after 5+ years of tests)

## Slide 10: Tsunamis: Black Swans or Grey Rhinos?
Black Swans
Extreme rarity: Black swan events are rare and unpredictable (outliers or exceptions to the norm).
Severe impact: Significant impact, widespread disruption and major changes in society or economy.
After-the-fact predictability: people come up with reasons why they should have been expected or could have been prevented.
Sumatra 2004, Japan 2011
Grey Rhinos
Moderate probability & straightforwardly predictable given current information.
However, they are neglected.
Several smaller, yet damaging and sometimes deadly tsunamis, continued to strike several regions worldwide in the last decades.
Chile 2010, 2014, Sulawesi 2018, Anak Krakatoa 2018, Greece-Turkey 2017, 2020, Kamçatka 2025…
And there will be others.
Notes: Extreme rarity: Black swan events are rare and unpredictable, and they occur much less frequently than other events. They are often seen as outliers or exceptions to the norm.
Severe impact: When a black swan event occurs, it has a significant impact on the world, causing widespread disruption and often leading to major changes in society or the economy.
After-the-fact predictability: Although black swan events are impossible to predict or forecast, people often try to explain them after they have occurred and come up with reasons why they should have been expected or could have been prevented.

## Slide 11: Some key points for discussion
Rapidity vs. Accuracy
The importance of current knowledge in a probabilistic framework
Real time simulations with HPC
The challenge of non-seismic tsunamis
The importance of being Tsunami Ready