## Slide 1: Rainfall-induced landslides and LEWS: Monitoring and local response strategies
Severine Bernardie (BRGM), Stefano Luigi Gariano (CNR-IRPI), Giovanna de Chiara (AB Appennino M.) - Marc Berenguer (UPC)
GOBEYOND, 2nd Workshop, Napoli (22 Apr 2026)

## Slide 2
Q1 - From emergency planning to early warning and response:
What are the key elements required to enable anticipation in robust LEWS, and how can the model efficiency be improved to forecast landslide occurrences at the relevant scales?

## Slide 3
Southern Apennines River Basin District Authority Autorità di Bacino Distrettuale dell’Appennino Meridionale
Angela DI PERNA, PhD, P.E. Giovanna DE CHIARA, PhD, P.E
Notes: Good morning everyone,
My name is Angela Di Perna, and I’m a Technical Officer at the Southern Apennines River Basin District Authority.
First of all, I would like to bring the greetings of our Secretary General, who apologizes for not being here today due to institutional commitments.
We are very pleased to have been invited to this interesting initiative.

## Slide 4
2000/60/EC Directive
D.L.vo 152/06, L. 221/15
2000/60/EC Directive
110 River Basin District in Europe
7 River Basin District in Italy
Southern Apennines River Basin District Authority
River Basin District (RBD)
an area of land and sea, made up of one or more adjacent river basins and their associated groundwater and coastal waters.
Integrated approach
Elements exposed to risk as key point
Risk Management
Public participation
The River Basin District (RBD)
The Southern Apennines River Basin District Authority is the public body that, within the framework of Directive 2000/60/EC and Legislative Decree 152/2006, adopts the river basin district as the reference physiographic unit for interpreting, governing, and planning in an integrated manner the relationship between water, soil, environment, and territory. This entails addressing, within a unified governance framework, issues that cannot be treated separately, including water management, landslides, floods, coastal erosion, the qualitative and quantitative status of water resources, land use, agroforestry criticalities, and the protection of environmental, landscape, and cultural heritage.
Strategic lines of the River Basin District Authority
Notes: Before addressing the main topic, I would like to briefly introduce our River Basin District Authority, that is a public body responsible for the management and protection of water resources within a river basin district, in accordance with the European Directive 2000/60/EC and national laws. Our District works over a large and complex area of about 67,000 square kilometers.
Therefore, we follow an integrated approach, considering water, soil, environment and land use as a whole connected system.
Our activities are based on four main lines: 1. planning and programming; 2. implementation of measures; 3. ensuring compatibility of local plans with district planning; 4. research and innovation.

## Slide 5
The River Basin Management Plan and the Management Plans constitute the instruments through which 'actions and land-use regulations' are planned and programmed, aimed at: the conservation, protection, and management of the soil; the protection of the qualitative and quantitative status of water resources; as well as the correct utilization of the physical system in correlation with the environmental, landscape, and cultural heritage and the structural and infrastructural system.
6
Hydrogeological Setting Plans – Hydraulic risk
6
Hydrogeological Setting Plans – Landslide risk
2
Costal erosion setting plan
Hydrogeological Setting Plans (PAI)
Planning, Programming and District Management
River Basin Management Plan (RBMP)
Notes: According to European regulations, we are responsible for preparing and updating Management Plans, which put the resources at the center as something to protect.
We also have to develop the Hydrogeological Setting Plans, which define land-use regulations and constraints.

## Slide 6
Sub-plans
Specific Projects
Concertation, communication, and computerization
Additional cross-functional activities
Osservatorio Permanente sugli Utilizzi Idrici
Contratti di Fiume
Il Sistema della Biodiversità
Tavoli Tecnici Trasferimenti Idrici Interregionali
Il Sistema Fisico di Riferimento
Beni Esposti e Vulnerabilità del Costruito
Il Sistema Cavità
Sistema di Monitoraggio Integrato
Il Sistema Paesaggio
Cartografia e Costruito
Il Fenomeni di Subsidenza
Progetto Sicurezza Idrica Sicurezza Sociale Idrostruttura dei Monti del Terminio Tuoro, vettore di trasporto e di distribuzione (Campania/Puglia)
Valutazione idromorfologica dei corsi d’acqua IDRAIM
Progettazione e realizzazione interventi per l’efficientamento dei sistema Dighe (Pertusillo, Conza, Saetta, Camastra, Acerenza, Genzano, Serra del Corvo, Monte Cotugno) – (Basilicata/Campania/Puglia) – Commissario Straordinario ex art. 1, comma 154, lett b), L. 145/2018
Progettazione e realizzazione della rete idropluviometrica delle aree del territorio Lucano
Attività per il recupero dei rifiuti in mare e nelle acque interne e per la promozione dell’economia circolare (Legge “SalvaMare”);
Analisi delle pressioni agenti sul sistema acque
Deflusso Ecologico
Progettazione interventi per sistema di adduzione e trasferimento Risorse Idriche;
Valutazione sui fabbisogni, usi (potabile, irriguo e industriale) e consumi
Progetti Pilota sui bacini del territorio Distrettuale per l’individuazione e progettazione di interventi integrati
Aggiornamento PAI e Piano interventi di mitigazione del rischio idrogeologico Casamicciola Terme – Ischia (Campania)
Aggiornamento PAI e Piano interventi di mitigazione del rischio idrogeologico altri Comuni di Ischia (Campania)
Mitigazione e Gestione del Rischio Idrogeologico nel Comune di Minori (Campania)
Progettazione e Realizzazione degli interventi di mitigazione del rischio idrogeologico (Campania/Lazio)
Interventi di Manutenzione Idraulica su areali di corpi idrici ricadenti nel distretto.
Progettazione e Realizzazione degli interventi di difesa e tutela del Fiume Mingardo (Campania)
DEDICA: Database Eventi di Dissesto Idrogeologico in Calabria
Intrusione del Cuneo Salino
Master Plan per la difesa, tutela e riqualificazione del Basso Volturno
Indirizzi operativi per l’adeguamento degli strumenti urbanistici ai contenuti e alle disposizioni dei Piani per la gestione del Rischio Idrogeologico
Bilancio Idrologico, Idrogeologico- Idrico e relativa progettazione e realizzazione (integrazione rete di monitoraggio) sull’intera area distrettuale
Nuova Cartografia e Nuovo rilievo Lidar
Specific projects, sub-plans, cross-functional actions
Notes: In addition, we carry out several specific projects, including monitoring systems and projects focused on risk mitigation.

## Slide 7
3 main phases
Risk Analysis
Hazard Analysis, Consequence Analysis, Risk Estimation
Risk Assessment
Risk acceptability and tolerability criteria
Risk Mitigation
Definition and implementation of structural and non-structural measures
The path to managing hydrogeological risk
(Fell et al., 2005; 2008)
analyze the physical processes, identify possible hazard scenarios, and understand what can happen and where.
Notes: In hydrogeological risk management, risk analysis is one of our main tasks. It includes the study of hazard, consequences, and risk.
In this phase, we analyze the physical processes, identify possible hazard scenarios, and understand what can happen and where.
Then, we move to risk assessment. Finally, we work on risk mitigation, which includes the program of measures.

## Slide 8
TOP-DOWN APPROACH
Multiscalar approach
From the general to the particular
Progressive Refinements
Gradual deepening of knowledge:
consistent and step-by-step knowledge base, starting from the large territory and moving to more detailed levels when needed.
Resource Optimization
Efficient use of data, time and economic resources
Institutional Governance
Multidisciplinary, Multiscalar & Circular Methodological Approach
Geotechnical Engineers
Hydraulic Engineers
Hydrologists
Urban planners
Structuralists
Geologists
Agronomists
Economists
IT specialists
Psychologists
Others
Shared methodology at different scales of analysis
Scales of analysis and restitution
Notes: To achieve these goals, we use a multidisciplinary and multi-scale approach.
In such a large area, it is important to improve our knowledge step by step, moving from general studies to more detailed and site-specific analyses.
In this way, we better understand natural processes, define risk scenarios, and support effective planning and mitigation measures.

## Slide 9
Scale 1:600.000
I Geologica I Livello: Schema Tettonico
Geologica II Livello: Macro Unità Tetton.
Geologica III Livello: Unità Tettoniche
Carta Geolitologica
Gradi di Permeabilità
Geomorfologia
Coperture
Scale 1:100.000
Carta Geolitologica
Complessi Idrogeologici
Grado di Permeabilità
Coperture
Geomorfologia
Frane
Scale 1:25.000
Carta Geolitologica
Complessi Idrogeologici
Grado di Permeabilità
Coperture
Geomorfologia
Frane
Themes
Geology
Geolithology
Hydrology
Permeability
Soil covers
Geomorphology
Landslides inventory
What are the key elements required to enable anticipation in robust LEWS?
… The knowledge
There is no reliable early warning system if we do not understand:
how the physical system works, its balance, and what can cause instability.
Notes: A key point in our work is knowledge. There is no reliable early warning system if we do not understand: how the physical system works, its balance, and what can cause instability.
For example, updating geological, geomorphological, and hydrological data at different scales can help to build a solid knowledge base.
This is important not only for planning, but also for designing effective monitoring systems.

## Slide 10
The pilot study of the hydrogeological risk management in the Municipality of Minori
The conceptual model for landslides scenarios
Rainfall-induced landslide in Minori
The Municipality of Minori, similarly to the other municipalities along the Amalfi Coast, is affected by extensive and significant hydrogeological issues. This is evidenced by the countless landslide events recorded in the past, which have caused severe damage to structural and infrastructural assets, as well as to historical and cultural heritage, and have resulted in numerous loss of human lives.
Knowledge helped us design a better monitoring system and improve the early warning system.
Notes: A clear example is the pilot study in the Municipality of Minori, located in the Amalfi coast.
In this case, Knowledge helped us design a better monitoring system and improve early warning system.
All this was done using a multidisciplinary and multi-scale approach.

## Slide 11
Rainfall-induced landslide in Minori
The Municipality of Minori, similarly to the other municipalities along the Amalfi Coast, is affected by extensive and significant hydrogeological issues. Short and intense rainfall events are frequent and can trigger flow-like landslides.
For this reason, an early warning system based only on rain gauges and daily rainfall averages is not enough for forecasting and alerts.In this case, knowledge helped us design a local monitoring network and consider the use of X-band radar technology.
The pilot study of the hydrogeological risk management in the Municipality of Minori
Notes: In this area, short and intense rainfall events are frequent and can trigger flow-like landslides.
For this reason, an early warning system based only on rain gauges and daily rainfall averages is not enough for forecasting and alerts.
In this case, knowledge helped us design a local monitoring network and consider the use of X-band radar technology.

## Slide 12
Conclusions
improving LEWS does not only mean improving the forecasting model
we need to improve knowledge, with a multidisciplinary and multi-scale approach
Only in this way we can design good monitoring systems, make models more effective, and produce forecasts that are really useful for operations
Notes: In conclusion, we believe that improving LEWS does not only mean improving the forecasting model. First of all, we need to improve knowledge, with a multidisciplinary and multi-scale approach
Only in this way we can design good monitoring systems, make models more effective, and produce forecasts that are really useful for operations

## Slide 13
Earthquake Early Warning may not be feasible nor useful everywhere
Importance of Earthquake Rapid Response to limit the impact of the event and to improve recovery
Earthquake Rapid Response tools are useful to:
  size up the global impact of the event (scaling of emergency response levels)
  estimate quantitative spatial indicators (support to first responders for deployment of teams and resources)
Objective: develop shallow landslide and debris flow forecasting model
Analysis and quantification of landslide hazard triggered by rainfall events, for designing EWS -> Different components of this analysis addressed :
- Quantification of rainfall triggering landslides
- Rainfall threshold definition
-> based on Landslide inventory & Meteorological data
- Spatialized threshold, integrating local geomorphological features
-> integrating shallow landslide susceptibility mapping
- Integrate the propagation of the landslides
    - Couple precipitation forecasts with: i) trigger thresholds; ii) susceptibility maps; iii) propagation of phenomena
LEWS development
This work is financed by the ANR VIGIMONT project VIGIlance MONTagne – Mountain Vigilance : Forecasting the risk of landslides and debris flows in mountainous areas ANR-22-CE04-0021. https://vigimont.fr/ ) and by France 2030 IRIMONT project (ANR-22-EXIR-0003)

## Slide 14
Impact of Extreme Rainfall on Triggering Conditions and Susceptibility for Shallow landslides
Departmental analysis (French Alps Maritime):
inventory comprising 5383 shallow landslides
Three types of landslides: road embankment, mid-slope and flow-like landslides.
Extreme event :Alex storm event (October 2020)
> 500 mm en 24h
Tinée, Vésubie and Roya valleys impacted
1656 induced landslides
text
Armand et al., NHESS, under review

## Slide 15
Data: COMEPHORE rainfall data (Météo-France)
radar data available since 1997 at an hourly time step on a regular grid of 1*1 km, resulting from the fusion of radar measurements and in situ observations from a rain gauge network
Model : Algorithme CTRL-T (Melillo and al. 2015, 2018)
Define rainfall events that trigger landslides, caracterised by :
  Cumulative rainfall (mm)
  Event duration(h)
E-D threshold : through a frequentist approach combined with bootstrapping
-> definition of 5% non-exceedance probability threshold
Highlight the impact of extreme events in EWS
ED threshold calculated, include Storm Alex-induced landslides (black threshold) and without, (grey threshold )
Impact of Extreme Rainfall on Triggering Conditions
Armand et al., NHESS, under review

## Slide 16
17 predisposing factors :
Parameters deriving from elevation model slope, aspect, curvature, TPI, landforms (Iwashi and Pike, and Weiss),
Lithology, clay, sand and silt content
Landcover
Model : Random Forest approach (Breiman, 2001)
Susceptibility maps computed a) From dataset excluding Storm Alex-induced landslides, and (b) From dataset including these landslides
Necessity to carefully consider extreme events in designing EWS
Impact of Extreme Rainfall on
Susceptibility mapping
Armand et al., NHESS,
under review

## Slide 17
Earthquake Early Warning may not be feasible nor useful everywhere
Importance of Earthquake Rapid Response to limit the impact of the event and to improve recovery
Earthquake Rapid Response tools are useful to:
  size up the global impact of the event (scaling of emergency response levels)
  estimate quantitative spatial indicators (support to first responders for deployment of teams and resources)
Next challenges
precipitation forecasts
landslide forecasts
Integrate in real-time landslide warning maps into decision
support systems (Wikipredict platform)
Consider propagation of the phenomena, at regional scale, and at local scale for some specific sites
Importance to jointly consider predisposing (geomorphology) and triggering (meteorological) factors
Considering additional meteorological factors : saturation, intensity, antecedent rainfall…)
Choice of alert levels (true positive versus false positive)
-> messages, and associated actions at the adequate spatial resolution, according to uncertainties

## Slide 18
Alert zone (Zone d’allertamento) |  |  |  | 
 | Area (km2) | Landslides (#) | Density (#/100 km2) | %
Mar-1 | 1359 | 97 (64) | 7.1 | 7.9
Mar-2 | 1300 | 208 (142) | 16.0 | 17.1
Mar-3 | 1214 | 131 (80) | 10.8 | 10.7
Mar-4 | 1904 | 243 (148) | 12.8 | 19.9
Mar-5 | 1602 | 230 (125) | 14.4 | 18.8
Mar-6 | 2003 | 312 (144) | 15.6 | 25.6
Marche

## Slide 19
Alert Zone | Alert messages (2017-2024) |  | 
 | Yellow Ordinary | Orange Moderate | Red High
Marche-1 | 260 | 16 | 0
Marche-2 | 245 | 18 | 0
Marche-3 | 268 | 16 | 0
Marche-4 | 252 | 19 | 0
Marche-5 | 253 | 12 | 0
Marche-6 | 228 | 15 | 0
Alert Zone | Skill Scores |  | 
 | TPR | FPR | TSS (HK)
Marche-1 | 0.60 | 0.06 | 0.54
Marche-2 | 0.62 | 0.05 | 0.57
Marche-3 | 0.50 | 0.07 | 0.43
Marche-4 | 0.54 | 0.05 | 0.48
Marche-5 | 0.42 | 0.06 | 0.36
Marche-6 | 0.45 | 0.05 | 0.40

## Slide 20
slope units

## Slide 21
municipalities

## Slide 22
Q2 – On the challenge of integrating landslide warnings into EM protocols:
What are the current operational setups connecting LEWS with Civil Protection? What are the challenges of translating landslide forecasts into decisive actions on the ground, integrating them into cross-agency Standard Operating Procedures?

## Slide 23
Southern Apennines River Basin District Authority Autorità di Bacino Distrettuale dell’Appennino Meridionale
Angela DI PERNA, PhD, P.E. Giovanna DE CHIARA, PhD, P.E

## Slide 24
The Municipality of Minori, similarly to the other municipalities along the Amalfi Coast, is affected by extensive and significant hydrogeological issues. This is evidenced by the countless landslide events recorded in the past, which have caused severe damage to structural and infrastructural assets, as well as to historical and cultural heritage, and have resulted in numerous loss of human lives.
The pilot study of the hydrogeological risk management in the Municipality of Minori
Notes: With reference to the second question, As previously introduced, it must be based on knowledge of the landslide scenarios that may occur within a given basin and at an appropriate territorial scale.
The existing monitoring networks, warning systems, meteorological and hydrogeological modelling tools, represent an essential basis for risk management. However, field experience tells us that these systems still show significant limits, especially when they have to support truly effective operational decisions on the ground.
Very often, these systems work at a scale that is too large compared to real processes.
They give useful information about the general level of risk, but they do not always capture the details of a single basin, a slope, or a specific urban or infrastructure area at risk. This is the key problem if we want forecasts to become real decisions in time, especially for local authorities like municipalities.
There is also the problem of turning forecasts into real actions, and doing it in time.
In coastal areas like the Amalfi Coast, escape routes are complex and not easy to use.
So, we need to understand if the warning time is enough to protect the population.
If evacuation needs more time, then earlier warnings are necessary.
If the area is difficult to access, activation thresholds must be defined very carefully.
If accessibility is complex, the monitoring system should be designed focusing on real operational needs

## Slide 25
Conclusions
The pilot project of Minori showed that the right approach is: from step-by-step knowledge system of the territory, to a better understanding of processes, better landslide scenarios, and better monitoring design.
The main challenge in turning forecasts into action is time. With intense rainfall, warning time is often very short and in complex areas, evacuation is difficult.
So, even if the forecast is correct, it may not be enough…
Notes: The pilot project of Minori showed that the right approach is: from step-by-step knowledge system of the territory, to a better understanding of processes, better landslide scenarios, and better monitoring design.
The main challenge in turning forecasts into action is time. With intense rain, warning time is often very short.
In complex areas, evacuation is difficult.
So, even if the forecast is correct, it may not be enough

## Slide 26
Every day, the Network of Functional Centers (Department of Civil Protection, Regions, and Autonomous Provinces) issues weather forecasts and assesses flood and landslide risks that could pose a danger to the population and cause damage.
If adverse effects or damage are expected, the Region or Autonomous Province issues a warning (yellow, orange, or red) for the affected areas. The Functional Centers continues to monitor weather conditions and their impact on the region.
Based on the alert, the Region and the Municipality assess which operational phase to activate (watch, pre-alert, alert) and carry out the actions outlined in their civil protection plans, coordinating their efforts. The Municipality informs the public and communicates the appropriate actions to take.
The weather and geo-hydrological Italian warning system

## Slide 28
Moving toward Impact-Based Forecasting: Instead of “Probability of rainfall / probability of landslides“ a forecast should be "High probability of ground effects on the national road SS18"

## Slide 29
Earthquake Early Warning may not be feasible nor useful everywhere
Importance of Earthquake Rapid Response to limit the impact of the event and to improve recovery
Earthquake Rapid Response tools are useful to:
  size up the global impact of the event (scaling of emergency response levels)
  estimate quantitative spatial indicators (support to first responders for deployment of teams and resources)
LEWS development through Vigimont project
Objective: Adress the different needs and acceptability of stakeholders regarding landslide EWS
Surveys conducted among stakeholders in charge of local civil protection, to gather qualitative data :
  risk perception,
  local risk prevention
  Current crisis management
  Needs
  28 qualitative surveys conducted through semi-structured interviews with safety and emergency actors
  118 quantitative surveys conducted with safety and emergency actors (municipality scale ( 86 questions)
Aurélie Arnaud, Audrey Borelly, Marseille University

## Slide 30
Map of current risk actors
Map of interactions between security actors
Map of information transfer
- Quantification of rainfall triggering
Interactions between actors, tools used and messages during crisis phase
Map of Interactions of civil protection and other actors
Map of security actors for Saint-Martin Vésubie municipality

## Slide 31
Need from risk actors of information on landslides
Short term landslide forecasting (hour to several hours)
Information on the phenomenon (description, delay….)
Damages, forecasting consequences
Guidelines, advices
Some results from existing crisis management actors
  Improve knowledge on what to do within crisis management at the municipality level (ex. Safeguarding plan activation…)
  colour of vigilance from Meteo France not understood -> delay in responses for municipality protection services
  Confusion in messages according to scale emission
  Territorial inequality regarding warning information

## Slide 32
Earthquake Early Warning may not be feasible nor useful everywhere
Importance of Earthquake Rapid Response to limit the impact of the event and to improve recovery
Earthquake Rapid Response tools are useful to:
  size up the global impact of the event (scaling of emergency response levels)
  estimate quantitative spatial indicators (support to first responders for deployment of teams and resources)
Presentation of these outputs to emergency managers and stakeholders
Departmental and regional civil protection
Inter municipalities
Municipalities
Co-construction of warning levels, messages, and associated actions at the municipality scale (within Safeguarding plan )
Next steps
Associated actions at local scale

## Slide 33
Group photo: Meeting point at the stairs
Poster Discussions and Hands-On Exhibitions with Coffee